Hüseyin Temizkan, Salih Erbalta, Sergey KUlikov
Park Sensor

---
Arduino UNO
Multifunction Shield
Ultrasonic Sensor – HC-SR04
Used Hardware

---
HC-SR04 Ultrasonic Sensor
The sensor will be triggered using 10µs of trigger signal.
Sensor sends a sonic burst and receives the reflecting sound waves
An Input signal will be received through Echo pin.
The distance will be calculated using the time difference between trigger and input signal

---
Calculating the Distance
The distance will be calculated using the time difference between the trigger and echo signal using timer overflows.
Basic Formula for the calculation:
Distance = number of overflows/ 58 cm
We count the number of overflows that are 16us and divide it by 58 to get the distance in cm.

---
Circuit
Trigger pin is connected to PD0 and set as output
Echo pin is connected to PD1 and set as input with no pullup resistor.
VCC and GND pins are connected accordingly.

---
Thank you for your attention!